## Slide 1: The Processor (2/3)
Chapter 4 (2/3)
Microprocessor Design and Application
마이크로 프로세서 설계 및 응용
2017 Spring
Minseong Kim (김민성)

## Slide 2: Major topics
Chapter 1: Computer Abstractions and Technology
Chapter 2: Instructions: Language of the Computer
Chapter 3: Arithmetic for Computers
Chapter 4: The Processor
Chapter 5: Large and Fast: Exploiting Memory Hierarchy
Chapter 6: Parallel Processors from Client to Cloud

## Slide 3: MIPS Pipelined Datapath
WB
MEM
Right-to-left flow leads to hazards

## Slide 4: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 5: Pipeline Operation
Cycle-by-cycle flow of instructions through the pipelined datapath
  “Single-clock-cycle” pipeline diagram
    Shows pipeline usage in a single cycle
    Highlight resources used
  c.f. “multi-clock-cycle” diagram
    Graph of operation over time
We’ll look at “single-clock-cycle” diagrams for load & store

## Slide 6: IF for Load, Store, …

## Slide 7: ID for Load, Store, …

## Slide 8: EX for Load

## Slide 9: MEM for Load

## Slide 10: WB for Load

## Slide 11: Corrected Datapath for Load

## Slide 12: EX for Store

## Slide 13: MEM for Store

## Slide 14: WB for Store

## Slide 15: Multi-Cycle Pipeline Diagram
Form showing resource usage

## Slide 16: Multi-Cycle Pipeline Diagram
Traditional form

## Slide 17: Single-Cycle Pipeline Diagram
State of pipeline in a given cycle

## Slide 18: Pipelined Control (Simplified)

## Slide 19: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation

## Slide 20: Pipelined Control

## Slide 21: Data Hazards in ALU Instructions
Consider this sequence:
  sub $2, $1,$3 and $12,$2,$5 or $13,$6,$2 add $14,$2,$2 sw $15,100($2)
We can resolve hazards with forwarding
  How do we detect when to forward?

## Slide 22: Dependencies & Forwarding

## Slide 23: Dependencies & Forwarding

## Slide 24: Detecting the Need to Forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs = register number for Rs sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs, ID/EX.RegisterRt
Data hazards when
  1a. EX/MEM.RegisterRd = ID/EX.RegisterRs
  1b. EX/MEM.RegisterRd = ID/EX.RegisterRt
  2a. MEM/WB.RegisterRd = ID/EX.RegisterRs
  2b. MEM/WB.RegisterRd = ID/EX.RegisterRt

## Slide 25: Detecting the Need to Forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite
And only if Rd for that instruction is not $zero
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 26: Forwarding Paths

## Slide 27: Forwarding Conditions
EX hazard
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) ForwardA = 10
  if (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) ForwardB = 10
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 28: Double Data Hazard
Consider the sequence:
  add $1,$1,$2 add $1,$1,$3 add $1,$1,$4
Both hazards occur
  Want to use the most recent
Revise MEM hazard condition
  Only fwd if EX hazard condition isn’t true

## Slide 29: Revised Forwarding Condition
MEM hazard
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRs)) and (MEM/WB.RegisterRd = ID/EX.RegisterRs)) ForwardA = 01
  if (MEM/WB.RegWrite and (MEM/WB.RegisterRd ≠ 0) and not (EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0) and (EX/MEM.RegisterRd = ID/EX.RegisterRt)) and (MEM/WB.RegisterRd = ID/EX.RegisterRt)) ForwardB = 01

## Slide 30: Datapath with Forwarding

## Slide 31: Load-Use Data Hazard

## Slide 32: Load-Use Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs, IF/ID.RegisterRt
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRt = IF/ID.RegisterRs) or (ID/EX.RegisterRt = IF/ID.RegisterRt))
If detected, stall and insert bubble

## Slide 33: How to Stall the Pipeline
Force control values in ID/EX register to 0
  EX, MEM and WB do nop (no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for lw
    Can subsequently forward to EX stage

## Slide 34: Stall/Bubble in the Pipeline
Stall inserted here

## Slide 35: Stall/Bubble in the Pipeline
Or, more accurately…

## Slide 36: Datapath with Hazard Detection

## Slide 37: Stalls and Performance
Stalls reduce performance
  But are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure